A FHIR IG Toolchain

---
The Tool Chain
- Access database
  - Input for script
    - FHIR specs, IG parameters, StructDef (Profiles and Extensions) parameters (mappings), ConceptMaps, ValueSets
- Script
  - Takes input and generated actual FHIR DSTU 2 StructureDefinition, ConceptMap, ValueSet and ImplementationGuide parts that is input for the next step
- IG Publisher
  - Takes the output from step 2 and generates the IG Publication

---
System pre-reqs
- Access – some access version that can export a table as XML
- Script – node.js
  - + Git checkout...
- IG Publisher
  - See ...

---
Access req’d tables input for Script
- VistA_FHIR_Map – for mappings and extensions
  - This is the core of the input. Here is the info that will populate the StructureDefinitions for Profiles and Extensions fields.
- ValueSetMembership (Query version)
  - This content will result in a ValueSet instances
- ConceptMap
  - This content will result in ConceptMap instances
- lookup – for groups and descriptions
  - Here is the info for the Artifact Groups and for Descriptions of the Groups (Coversheet Area) and Profiles.
- fhirProperties – for type info of the extensions and for type info and existing attributes of resources

---
Messages
- The Script does some checking and generates messages on issues
- The IG Publisher does more checking and generates issues when running and generates a QA report with messages

---
Steps
- Export the named tables as XML, n.b. filenames are fixed for the script
- Place them in the script/input folder
- Run the script/vfm2sd.js
- Copy the script/output contents to the input/resources folder of the sample-ig
- Run the IG Publisher
- Publish the HTML

---
Script Messages
- 3 levels, WARN, INFO and ERROR
- INFO is just fyi
- WARN are possible issues, may cause problems in IG
- ERROR are issues that will cause problems and are ignored, look here if you miss content in the IG
- N.B. All messages always start with associated ID1 of the VistA_FHIR_Map row.

---
Script: WARN messages
- ${profileId} DUPLICATE fixed value '${fixedElementPath}'
  - There are >1 fixed values specified for an attribute.
    *** Is this supposed to be a valueset?
- ${profileId} AUTO <type> '${extraElementPath}'
  - ...
- no mappings found in ${profileId}; no profile written
  - Profile is defined, but there are no mappings?
- fixedElementPath '${fixedElementPath}' is a non existing path? No info on type, default to String
  - This path is missing from fhirProperties.xml input file or really invalid.
- ${profileId} IGNORE invalid fixed value format: '${propline}'
  - Fixed value line format is “<full primitive attribute path>=<value>”
- ConceptMap '${name}' row without target mapping ignored
  - Concept mappings need a source and a target.

---
Script: ERROR messages
- missing path | missing field name | missing resource name | missing property name
  - The VistA_FHIR_Map row misses some required field values
- resourceName '${resourceName}' not an existing resource
  - There is a list of expected resource names in the script and this one is not on it.
- resourceName '${resourceName}' is different from constrainedType '${sd.constrainedType}'?
  - Resource Name of this mapping line is different from the first mapping line. Profiles can only constrain 1 Resource Type.
- elementPath '${elementPath}' not a valid path | fixedElementPath '${fixedElementPath}' not a valid path
  - Check the path. Each segment (between the dots) should start with a letter followed by letters, numbers, minus.
- fixedElementPath '${fixedElementPath}' cannot set fixed value for non primitive type ${fixedType}
  - Fixed values are only possible for primitive types. It the path a full primitive attribute path?
- ${profileId} type[x] missing for '${elementPath}' | expect type specified '${elementPath}'
  - This is a [x] path and for profiles the type must be specified.
- extname "${extname}" not a valid FHIR id | profileId '${profileId}' not a valid FHIR id | ValueSet '${name}' not a valid FHIR id | ConceptMap '${name}' not a valid FHIR id
  - Check the name, must be a letters, numbers, minus, or dot, spaces are not allowed.

---
Links
- Script: https://github.com/mvdzel/vha-ampl-fhir-ig
- IG Publisher:
  - https://github.com/FHIR/latest-ig-publisher
  - https://confluence.hl7.org/display/FHIR/IG+Publisher+Documentation